## Slide 1: Lecture 1.2 – Course Introduction
Introduction to Heterogeneous Parallel Computing
Accelerated Computing
GPU Teaching Kit

## Slide 2: Objectives
To learn the major differences between latency devices (CPU cores) and throughput devices (GPU cores)
To understand why winning applications increasingly use both types of devices

## Slide 3: Heterogeneous Parallel Computing
Use the best match for the job (heterogeneity in mobile SOC)
Latency Cores
Throughput Cores
DSP Cores
HW IPs
Configurable
Logic/Cores
On-chip Memories
Cloud Services

## Slide 4: CPU and GPU are designed very differently
CPU
Latency Oriented Cores
Chip
Core
Local Cache
Registers
SIMD Unit
Control
GPU
Throughput Oriented Cores
Chip
Compute Unit
Cache/Local Mem
Registers
SIMD Unit
Threading

## Slide 5: CPUs: Latency Oriented Design
Powerful ALU
  Reduced operation latency
Large caches
  Convert long latency memory accesses to short latency cache accesses
Sophisticated control
  Branch prediction for reduced branch latency
  Data forwarding for reduced data latency
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU

## Slide 6: GPUs: Throughput Oriented Design
Small caches
  To boost memory throughput
Simple control
  No branch prediction
  No data forwarding
Energy efficient ALUs
  Many, long latency but heavily pipelined for high throughput
Require massive number of threads to tolerate latencies
  Threading logic
  Thread state
DRAM
GPU

## Slide 7: Winning Applications Use Both CPU and GPU
CPUs for sequential parts where latency matters
  CPUs can be 10X+ faster than GPUs for sequential code
GPUs for parallel parts where throughput wins
  GPUs can be 10X+ faster than CPUs for parallel code

## Slide 8: GPU computing reading resources
  90 articles in two volumes

## Slide 9: Heterogeneous Parallel Computing in Many Disciplines
Financial Analysis
Scientific Simulation
Engineering Simulation
Data Intensive Analytics
Medical Imaging
Digital Audio Processing
Computer Vision
Digital Video Processing
Biomedical Informatics
Electronic Design Automation
Statistical Modeling
Ray Tracing Rendering
Interactive Physics
Numerical Methods

## Slide 10
GPU Teaching Kit
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.
Accelerated Computing