## Slide 1: Module 12 – Floating-Point Considerations
Lecture 12.1 - Floating-Point Precision and Accuracy

## Slide 2: Objective
To understand the fundamentals of floating-point representation
To understand the IEEE-754 Floating Point Standard
CUDA GPU Floating-point speed, accuracy and precision
  Cause of errors
  Algorithm considerations
  Accuracy of device runtime functions
  -fastmath compiler option
  Future performance considerations
Notes: fdfsdf

## Slide 3: What is IEEE floating-point format?
An industrywide standard for representing floating-point numbers to ensure that hardware from different vendors generate results that are consistent with each other
A floating point binary number consists of three parts:
  sign (S), exponent (E), and mantissa (M)
  Each (S, E, M) pattern uniquely identifies a floating point number
For each bit pattern, its IEEE floating-point value is derived as:
  value = (-1)S * M * {2E}, where 1.0 ≤ M < 10.0B
The interpretation of S is simple: S=0 results in a positive number and S=1 a negative number

## Slide 4: Normalized Representation
Specifying that 1.0B ≤ M < 10.0B makes the mantissa value for each floating point number unique.
  For example, the only mantissa value allowed for 0.5D is M =1.0
    0.5D = 1.0B * 2-1
  Neither 10.0B * 2 -2 nor 0.1B * 2 0 qualifies
Because all mantissa values are of the form 1.XX…, one can omit the “1.” part in the representation.
  The mantissa value of 0.5D in a 2-bit mantissa is 00, which is derived by omitting “1.” from 1.00.
  Mantissa without implied 1 is called the fraction

## Slide 5: Exponent Representation
In an n-bit exponent representation, 2n-1-1 is added to its 2's complement representation to form its excess representation.
  See Table for a 3-bit exponent representation
A simple unsigned integer comparator can be used to compare the magnitude of two FP numbers
Symmetric range for +/- exponents (111 reserved)
2’s complement | Actual decimal | Excess-3
000 | 0 | 011
001 | 1 | 100
010 | 2 | 101
011 | 3 | 110
100 | (reserved pattern) | 111
101 | -3 | 000
110 | -2 | 001
111 | -1 | 010

## Slide 6: A simple, hypothetical 5-bit FP format
2’s complement | Actual decimal | Excess-1
00 | 0 | 01
01 | 1 | 10
10 | (reserved pattern) | 11
11 | -1 | 00
Assume 1-bit S, 2-bit E, and 2-bit M
  0.5D = 1.00B * 2-1
  0.5D = 0 00 00, where S = 0, E = 00, and M = (1.)00

## Slide 7: Representable Numbers
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
The representable numbers of a given format is the set of all numbers that can be exactly represented in the format.
See Table for representable numbers of an unsigned 3-bit integer format
0
7
1
4
2
3
5
6
-1
9
8

## Slide 8: Representable Numbers of a 5-bit Hypothetical IEEE Format
 |  | Non-zero |  | Abrupt underflow |  | Gradual underflow | 
E | M | S=0 | S=1 | S=0 | S=1 | S=0 | S=1
00 | 00 | 2-1 | -(2-1) | 0 | 0 | 0 | 0
 | 01 | 2-1+1*2-3 | -(2-1+1*2-3) | 0 | 0 | 1*2-2 | -1*2-2
 | 10 | 2-1+2*2-3 | -(2-1+2*2-3) | 0 | 0 | 2*2-2 | -2*2-2
 | 11 | 2-1+3*2-3 | -(2-1+3*2-3) | 0 | 0 | 3*2-2 | -3*2-2
01 | 00 | 20 | -(20) | 20 | -(20) | 20 | -(20)
 | 01 | 20+1*2-2 | -(20+1*2-2) | 20+1*2-2 | -(20+1*2-2) | 20+1*2-2 | -(20+1*2-2)
 | 10 | 20+2*2-2 | -(20+2*2-2) | 20+2*2-2 | -(20+2*2-2) | 20+2*2-2 | -(20+2*2-2)
 | 11 | 20+3*2-2 | -(20+3*2-2) | 20+3*2-2 | -(20+3*2-2) | 20+3*2-2 | -(20+3*2-2)
10 | 00 | 21 | -(21) | 21 | -(21) | 21 | -(21)
 | 01 | 21+1*2-1 | -(21+1*2-1) | 21+1*2-1 | -(21+1*2-1) | 21+1*2-1 | -(21+1*2-1)
 | 10 | 21+2*2-1 | -(21+2*2-1) | 21+2*2-1 | -(21+2*2-1) | 21+2*2-1 | -(21+2*2-1)
 | 11 | 21+3*2-1 | -(21+3*2-1) | 21+3*2-1 | -(21+3*2-1) | 21+3*2-1 | -(21+3*2-1)
11 | Reserved pattern |  |  |  |  |  | 
Cannot Represent Zero!

## Slide 9: Flush to Zero
Treat all bit patterns with E=0 as 0.0
  This takes away several representable numbers near zero and lump them all into 0.0
  For a representation with large M, a large number of representable numbers will be removed
1
2
3
4
0

## Slide 10: Flush to Zero
 |  | No-zero |  | Flush to Zero |  | Denormalized | 
E | M | S=0 | S=1 | S=0 | S=1 | S=0 | S=1
00 | 00 | 2-1 | -(2-1) | 0 | 0 | 0 | 0
 | 01 | 2-1+1*2-3 | -(2-1+1*2-3) | 0 | 0 | 1*2-2 | -1*2-2
 | 10 | 2-1+2*2-3 | -(2-1+2*2-3) | 0 | 0 | 2*2-2 | -2*2-2
 | 11 | 2-1+3*2-3 | -(2-1+3*2-3) | 0 | 0 | 3*2-2 | -3*2-2
01 | 00 | 20 | -(20) | 20 | -(20) | 20 | -(20)
 | 01 | 20+1*2-2 | -(20+1*2-2) | 20+1*2-2 | -(20+1*2-2) | 20+1*2-2 | -(20+1*2-2)
 | 10 | 20+2*2-2 | -(20+2*2-2) | 20+2*2-2 | -(20+2*2-2) | 20+2*2-2 | -(20+2*2-2)
 | 11 | 20+3*2-2 | -(20+3*2-2) | 20+3*2-2 | -(20+3*2-2) | 20+3*2-2 | -(20+3*2-2)
10 | 00 | 21 | -(21) | 21 | -(21) | 21 | -(21)
 | 01 | 21+1*2-1 | -(21+1*2-1) | 21+1*2-1 | -(21+1*2-1) | 21+1*2-1 | -(21+1*2-1)
 | 10 | 21+2*2-1 | -(21+2*2-1) | 21+2*2-1 | -(21+2*2-1) | 21+2*2-1 | -(21+2*2-1)
 | 11 | 21+3*2-1 | -(21+3*2-1) | 21+3*2-1 | -(21+3*2-1) | 21+3*2-1 | -(21+3*2-1)
11 | Reserved pattern |  |  |  |  |  | 

## Slide 11: Why is flushing to zero problematic?
Many physical model calculations work on values that are very close to zero
  Dark (but not totally black) sky in movie rendering
  Small distance fields in electrostatic potential calculation
  …
Without Denormalization, these calculations tend to create artifacts that compromise the integrity of the models

## Slide 12: Denormalized Numbers
The actual method adopted by the IEEE standard is called “denormalized numbers” or “gradual underflow”.
  The method relaxes the normalization requirement for numbers very close to 0.
  Whenever E=0, the mantissa is no longer assumed to be of the form 1.XX. Rather, it is assumed to be 0.XX. In general, if the n-bit exponent is 0, the value is 0.M * 2 - 2 ^(n-1) + 2
0
1
2
3

## Slide 13: Denormalization
 |  | No-zero |  | Flush to Zero |  | Denormalized | 
E | M | S=0 | S=1 | S=0 | S=1 | S=0 | S=1
00 | 00 | 2-1 | -(2-1) | 0 | 0 | 0 | 0
 | 01 | 2-1+1*2-3 | -(2-1+1*2-3) | 0 | 0 | 1*2-2 | -1*2-2
 | 10 | 2-1+2*2-3 | -(2-1+2*2-3) | 0 | 0 | 2*2-2 | -2*2-2
 | 11 | 2-1+3*2-3 | -(2-1+3*2-3) | 0 | 0 | 3*2-2 | -3*2-2
01 | 00 | 20 | -(20) | 20 | -(20) | 20 | -(20)
 | 01 | 20+1*2-2 | -(20+1*2-2) | 20+1*2-2 | -(20+1*2-2) | 20+1*2-2 | -(20+1*2-2)
 | 10 | 20+2*2-2 | -(20+2*2-2) | 20+2*2-2 | -(20+2*2-2) | 20+2*2-2 | -(20+2*2-2)
 | 11 | 20+3*2-2 | -(20+3*2-2) | 20+3*2-2 | -(20+3*2-2) | 20+3*2-2 | -(20+3*2-2)
10 | 00 | 21 | -(21) | 21 | -(21) | 21 | -(21)
 | 01 | 21+1*2-1 | -(21+1*2-1) | 21+1*2-1 | -(21+1*2-1) | 21+1*2-1 | -(21+1*2-1)
 | 10 | 21+2*2-1 | -(21+2*2-1) | 21+2*2-1 | -(21+2*2-1) | 21+2*2-1 | -(21+2*2-1)
 | 11 | 21+3*2-1 | -(21+3*2-1) | 21+3*2-1 | -(21+3*2-1) | 21+3*2-1 | -(21+3*2-1)
11 | Reserved pattern |  |  |  |  |  | 

## Slide 14: IEEE 754 Format and Precision
Single Precision
  1-bit sign, 8 bit exponent (bias-127 excess), 23 bit fraction
Double Precision
  1-bit sign, 11-bit exponent (1023-bias excess), 52 bit fraction
  The largest error for representing a number is reduced to 1/229 of single precision representation

## Slide 15: Special Bit Patterns
An ∞ can be created by overflow, e.g., divided by zero. Any representable number divided by +∞ or -∞ results in 0.
NaN (Not a Number) is generated by operations whose input values do not make sense, for example, 0/0, 0*∞, ∞/∞, ∞ - ∞.
  Also used to for data that has not been properly initialized in a program.
  Signaling NaNs (SNaNs) are represented with most significant mantissa bit cleared whereas quiet NaNs are represented with most significant mantissa bit set.
exponent | mantissa | meaning
11…1 | ≠ 0 | NaN
11…1 | =0 | (-1)S * ∞
00…0 | ≠0 | denormalized
00…0 | =0 | 0

## Slide 16: Floating Point Accuracy and Rounding
The accuracy of a floating point arithmetic operation is measured by the maximal error introduced by the operation.
The most common source of error in floating point arithmetic is when the operation generates a result that cannot be exactly represented and thus requires rounding.
Rounding occurs if the mantissa of the result value needs too many bits to be represented exactly.

## Slide 17: Rounding and Error
Assume our 5-bit representation, consider
1.0*2-2 (0, 00, 01) + 1.00*21 (0, 10, 00)
The hardware needs to shift the mantissa bits in order to align the correct bits with equal place value
0.001*21 (0, 00, 0001) + 1.00*21 (0, 10, 00)
The ideal result would be 1.001 * 21 (0, 10, 001) but this would
require 3 mantissa bits!
exponent is 00 →denorm

## Slide 18: Rounding and Error
In some cases, the hardware may only perform the operation on a limited number of bits for speed and area cost reasons
  An adder may only have 3 bit positions in our example so the first operand would be treated as a 0.00
  0.001*21 (0, 00, 0001) + 1.00*21 (0, 10, 00)

## Slide 19: Error Measure
If a hardware adder has at least two more bit positions than the total (both implicit and explicit) number of mantissa bits, the error would never be more than half of the place value of the mantissa
  0.001 in our 5-bit format
We refer to this as 0.5 ULP (Units in the Last Place)
  If the hardware is designed to perform arithmetic and rounding operations perfectly, the most error that one should introduce should be no more than 0.5 ULP
  The error is limited by the precision for this case.

## Slide 20: Order of Operations Matter
Floating point operations are not strictly associative
The root cause is that some times a very small number can disappear when added to or subtracted from a very large number.
  (Large + Small) + Small ≠ Large + (Small + Small)

## Slide 21: Algorithm Considerations
Sequential sum
  1.00*20 +1.00*20 + 1.00*2-2 + 1.00*2-2
  = 1.00*21 + 1.00*2-2 + 1.00*2-2
  = 1.00*21 + 1.00*2-2
  = 1.00*21
Parallel reduction
(1.00*20 +1.00*20) + (1.00*2-2 + 1.00*2-2 )
= 1.00*21 + 1.00*2-1
= 1.01*21

## Slide 22: Runtime Math Library
There are two types of runtime math operations
  __func(): direct mapping to hardware ISA
    Fast but low accuracy
    Examples: __sin(x), __exp(x), __pow(x,y)
  func() : compile to multiple instructions
    Slower but higher accuracy (0.5 ulp, units in the least place, or less)
    Examples: sin(x), exp(x), pow(x,y)
The -use_fast_math compiler option forces every func() to compile to __func()
Notes: The error is measured in ulp (units in the last place), that is the values of the results are multiplied by a power of the base such that an error in the last significant place is an error of 1.

## Slide 23: Make your program float-safe!
Double precision likely have performance cost
  Careless use of double or undeclared types may run more slowly
Important to be explicit whenever you want single precision to avoid using double precision where it is not needed
  Add ‘f’ specifier on float literals:
    foo = bar * 0.123; // double assumed
    foo = bar * 0.123f; // float explicit
  Use float version of standard library functions
    foo = sin(bar); // double assumed
    foo = sinf(bar); // single precision explicit

## Slide 24
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.