## Slide 1: Module 14 – Efficient Host-Device Data Transfer
Lecture 14.1 - Pinned Host Memory

## Slide 2: Objective
To learn the important concepts involved in copying (transferring) data between host and device
  Direct Memory Access
  Pinned memory

## Slide 3: CPU-GPU Data Transfer using DMA
DMA (Direct Memory Access) hardware is used by cudaMemcpy() for better efficiency
  Frees CPU for other tasks
  Hardware unit specialized to transfer a number of bytes requested by OS
  Between physical memory address space regions (some can be mapped I/O memory locations)
  Uses system interconnect, typically PCIe in today’s systems
CPU Main Memory (DRAM)
GPU card
(or other I/O cards)
DMA
Global Memory
PCIe

## Slide 4: Virtual Memory Management
Modern computers use virtual memory management
  Many virtual memory spaces mapped into a single physical memory
  Virtual addresses (pointer values) are translated into physical addresses
Not all variables and data structures are always in the physical memory
  Each virtual address space is divided into pages that are mapped into and out of the physical memory
  Virtual memory pages can be mapped out of the physical memory (page-out) to make room
  Whether or not a variable is in the physical memory is checked at address translation time

## Slide 5: Data Transfer and Virtual Memory
DMA uses physical addresses
  When cudaMemcpy() copies an array, it is implemented as one or more DMA transfers
  Address is translated and page presence checked for the entire source and destination regions at the beginning of each DMA transfer
  No address translation for the rest of the same DMA transfer so that high efficiency can be achieved
The OS could accidentally page-out the data that is being read or written by a DMA and page-in another virtual page into the same physical location

## Slide 6: Pinned Memory and DMA Data Transfer
Pinned memory are virtual memory pages that are specially marked so that they cannot be paged out
Allocated with a special system API function call
a.k.a. Page Locked Memory, Locked Pages, etc.
CPU memory that serve as the source or destination of a DMA transfer must be allocated as pinned memory

## Slide 7: CUDA data transfer uses pinned memory.
The DMA used by cudaMemcpy() requires that any source or destination in the host memory is allocated as pinned memory
If a source or destination of a cudaMemcpy() in the host memory is not allocated in pinned memory, it needs to be first copied to a pinned memory – extra overhead
cudaMemcpy() is faster if the host memory source or destination is allocated in pinned memory since no extra copy is needed

## Slide 8: Allocate/Free Pinned Memory
cudaHostAlloc(), three parameters
  Address of pointer to the allocated memory
  Size of the allocated memory in bytes
  Option – use cudaHostAllocDefault for now
cudaFreeHost(), one parameter
    Pointer to the memory to be freed

## Slide 9: Using Pinned Memory in CUDA
Use the allocated pinned memory and its pointer the same way as those returned by malloc();
The only difference is that the allocated memory cannot be paged by the OS
The cudaMemcpy() function should be about 2X faster with pinned memory
Pinned memory is a limited resource
  over-subscription can have serious consequences

## Slide 10: Putting It Together - Vector Addition Host Code Example
int main()
{
float *h_A, *h_B, *h_C;
…
cudaHostAlloc((void **) &h_A, N* sizeof(float),
cudaHostAllocDefault);
cudaHostAlloc((void **) &h_B, N* sizeof(float),
cudaHostAllocDefault);
cudaHostAlloc((void **) &h_C, N* sizeof(float),
cudaHostAllocDefault);
…
// cudaMemcpy() runs 2X faster
}

## Slide 11
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.