## Slide 1: Lecture 3.5 – CUDA Parallelism Model
Thread Scheduling
Accelerated Computing
GPU Teaching Kit

## Slide 2: Objective
To learn how a CUDA kernel utilizes hardware execution resources
  Assigning thread blocks to execution resources
  Capacity constrains of execution resources
  Zero-overhead thread scheduling

## Slide 3: Transparent Scalability
Each block can execute in any order relative to others.
Hardware is free to assign blocks to any processor at any time
  A kernel scales to any number of parallel processors
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Thread grid
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
time

## Slide 4: Example: Executing Thread Blocks
Threads are assigned to Streaming Multiprocessors (SM) in block granularity
  Up to 8 blocks to each SM as resource allows
  Fermi SM can take up to 1536 threads
    Could be 256 (threads/block) * 6 blocks
    Or 512 (threads/block) * 3 blocks, etc.
SM maintains thread/block idx #s
SM manages/schedules thread execution
t0 t1 t2 … tm
Blocks
SP
Shared
Memory
SM

## Slide 5: The Von-Neumann Model
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Notes: Insert von-neumann schematic here

## Slide 6: The Von-Neumann Model with SIMD units
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Single Instruction Multiple Data
(SIMD)
Notes: Insert von-neumann schematic here

## Slide 7: Warps as Scheduling Units
Each Block is executed as 32-thread Warps
  An implementation decision, not part of the CUDA programming model
  Warps are scheduling units in SM
  Threads in a warp execute in SIMD
  Future GPUs may have different number of threads in each warp

## Slide 8: Warp Example
If 3 blocks are assigned to an SM and each block has 256 threads, how many Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0 Warps
Block 1 Warps
…
t0 t1 t2 … t31
…
Block 2 Warps
Register File
L1
Shared Memory

## Slide 9: Example: Thread Scheduling (Cont.)
SM implements zero-overhead warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution based on a prioritized scheduling policy
  All threads in a warp execute the same instruction when selected

## Slide 10: Block Granularity Considerations
For Matrix Multiplication using multiple blocks, should I use 8X8, 16X16 or 32X32 blocks for Fermi?
  For 8X8, we have 64 threads per Block. Since each SM can take up to 1536 threads, which translates to 24 Blocks. However, each SM can only take up to 8 Blocks, only 512 threads will go into each SM!
  For 16X16, we have 256 threads per Block. Since each SM can take up to 1536 threads, it can take up to 6 Blocks and achieve full capacity unless other resource considerations overrule.
  For 32X32, we would have 1024 threads per Block. Only one block can fit into an SM for Fermi. Using only 2/3 of the thread capacity of an SM.

## Slide 11
GPU Teaching Kit
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.