## Slide 1: Module 4.1 – Memory and Data Locality
CUDA Memories

## Slide 2: Objective
To learn to effectively use the CUDA memory types in a parallel program
  Importance of memory access efficiency
  Registers, shared memory, global memory
  Scope and lifetime

## Slide 3: Review: Image Blur Kernel.
// Get the average of the surrounding 2xBLUR_SIZE x 2xBLUR_SIZE box
for(int blurRow = -BLUR_SIZE; blurRow < BLUR_SIZE+1; ++blurRow) {
for(int blurCol = -BLUR_SIZE; blurCol < BLUR_SIZE+1; ++blurCol) {
int curRow = Row + blurRow;
int curCol = Col + blurCol;
// Verify we have a valid image pixel
if(curRow > -1 && curRow < h && curCol > -1 && curCol < w) {
pixVal += in[curRow * w + curCol];
pixels++; // Keep track of number of pixels in the accumulated total
}
}
}
// Write our new pixel value out
out[Row * w + Col] = (unsigned char)(pixVal / pixels);

## Slide 4: How about performance on a GPU
All threads access global memory for their input matrix elements
  One memory accesses (4 bytes) per floating-point addition
  4B/s of memory bandwidth/FLOPS
Assume a GPU with
  Peak floating-point rate 1,500 GFLOPS with 200 GB/s DRAM bandwidth
  4*1,500 = 6,000 GB/s required to achieve peak FLOPS rating
  The 200 GB/s memory bandwidth limits the execution at 50 GFLOPS
This limits the execution rate to 3.3% (50/1500) of the peak floating-point execution rate of the device!
Need to drastically cut down memory accesses to get close to the1,500 GFLOPS

## Slide 5: Example – Matrix Multiplication
M
N
P
BLOCK_WIDTH
WIDTH
WIDTH
BLOCK_WIDTHE
WIDTH
WIDTH
Row
Col

## Slide 6: A Basic Matrix Multiplication
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width) {
// Calculate the row index of the P element and M
int Row = blockIdx.y*blockDim.y+threadIdx.y;
// Calculate the column index of P and N
int Col = blockIdx.x*blockDim.x+threadIdx.x;
if ((Row < Width) && (Col < Width)) {
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k) {
Pvalue += M[Row*Width+k]*N[k*Width+Col];
}
P[Row*Width+Col] = Pvalue;
}
}

## Slide 7: Example – Matrix Multiplication
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width) {
// Calculate the row index of the P element and M
int Row = blockIdx.y*blockDim.y+threadIdx.y;
// Calculate the column index of P and N
int Col = blockIdx.x*blockDim.x+threadIdx.x;
if ((Row < Width) && (Col < Width)) {
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k) {
Pvalue += M[Row*Width+k]*N[k*Width+Col];
}
P[Row*Width+Col] = Pvalue;
}
}

## Slide 8: A Toy Example: Thread to P Data Mapping
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
Block(0,0)
Block(0,1)
Block(1,1)
Block(1,0)
BLOCK_WIDTH = 2
Thread(0,0)
Thread(1,0)
Thread(0,1)
Thread(1,1)

## Slide 9: Calculation of P0,0 and P0,1
P0,1
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
P0,0
M1,3
P1,0
N3,0
N3,1
N2,1
N1,1
N0,1
N0,0
N1,0
N2,0
P1,1
P0,1

## Slide 10: Memory and Registers in the Von-Neumann Model
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Notes: Insert von-neumann schematic here

## Slide 11: Programmer View of CUDA Memories
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
Notes: Global, constant, and texture memory contents are persistent across kernels called by the same application.
Each thread uses a number of registers.
Each block allocates a certain amount of Shared Memory that is accessible to all threads in the block.

## Slide 12: Declaring CUDA Variables
__device__ is optional when used with __shared__, or __constant__
Automatic variables reside in a register
  Except per-thread arrays that reside in global memory
Variable declaration | Memory | Scope | Lifetime
int LocalVar; | register | thread | thread
__device__ __shared__ int SharedVar; | shared | block | block
__device__ int GlobalVar; | global | grid | application
__device__ __constant__ int ConstantVar; | constant | grid | application

## Slide 13: Example: Shared Memory Variable Declaration
void blurKernel(unsigned char * in, unsigned char * out, int w, int h)
{
__shared__ float ds_in[TILE_WIDTH][TILE_WIDTH];
…
}

## Slide 14: Where to Declare Variables?
Can host access it?
Outside of any Function
In the kernel
global
constant
register
shared

## Slide 15: Shared Memory in CUDA
A special type of memory whose contents are explicitly defined and used in the kernel source code
  One in each SM
  Accessed at much higher speed (in both latency and throughput) than global memory
  Scope of access and sharing - thread blocks
  Lifetime – thread block, contents will disappear after the corresponding thread finishes terminates execution
  Accessed by memory load/store instructions
  A form of scratchpad memory in computer architecture

## Slide 16: Hardware View of CUDA Memories
Global Memory
Processing Unit
I/O
ALU
Processor (SM)
Shared Memory
Register
File
Control Unit
PC
IR
Notes: Insert von-neumann schematic here

## Slide 17
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.