## Slide 1: Module 4.4 - Memory and Data Locality
Tiled Matrix Multiplication Kernel

## Slide 2: Objective
To learn to write a tiled matrix-multiplication kernel
  Loading and using tiles for matrix multiplication
  Barrier synchronization, shared memory
  Resource Considerations
  Assume that Width is a multiple of tile size for simplicity
2

## Slide 3: Loading Input Tile 0 of M (Phase 0)
M
N
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Row
Col
Have each thread load an M element and an N element at the same relative position as its P element.
int Row = by * blockDim.y + ty;
int Col = bx * blockDim.x + tx;
2D indexing for accessing Tile 0:
M[Row][tx]
N[ty][Col]

## Slide 4: Loading Input Tile 0 of N (Phase 0)
M
N
P
BLOCK_WIDTH
WIDTH
WIDTH
BLOCK_WIDTHE
WIDTH
WIDTH
Row
Col
Have each thread load an M element and an N element at the same relative position as its P element.
int Row = by * blockDim.y + ty;
int Col = bx * blockDim.x + tx;
2D indexing for accessing Tile 0:
M[Row][tx]
N[ty][Col]

## Slide 5: Loading Input Tile 1 of M (Phase 1)
M
N
P
BLOCK_WIDTH
WIDTH
WIDTH
BLOCK_WIDTHE
WIDTH
WIDTH
Row
Col
2D indexing for accessing Tile 1:
M[Row][1*TILE_WIDTH + tx]
N[1*TILE*WIDTH + ty][Col]

## Slide 6: Loading Input Tile 1 of N (Phase 1)
M
N
P
BLOCK_WIDTH
WIDTH
WIDTH
BLOCK_WIDTHE
WIDTH
WIDTH
Row
Col
2D indexing for accessing Tile 1:
M[Row][1*TILE_WIDTH + tx]
N[1*TILE*WIDTH + ty][Col]

## Slide 7: M and N are dynamically allocated - use 1D indexing
M[Row][p*TILE_WIDTH+tx]
M[Row*Width + p*TILE_WIDTH + tx]
N[p*TILE_WIDTH+ty][Col]
N[(p*TILE_WIDTH+ty)*Width + Col]
where p is the sequence number of the current phase

## Slide 8: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, Int Width)
{
__shared__ float ds_M[TILE_WIDTH][TILE_WIDTH];
__shared__ float ds_N[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * blockDim.y + ty;
int Col = bx * blockDim.x + tx;
float Pvalue = 0;
// Loop over the M and N tiles required to compute the P element
for (int p = 0; p < n/TILE_WIDTH; ++p) {
// Collaborative loading of M and N tiles into shared memory
ds_M[ty][tx] = M[Row*Width + p*TILE_WIDTH+tx];
ds_N[ty][tx] = N[(t*TILE_WIDTH+ty)*Width + Col];
__syncthreads();
for (int i = 0; i < TILE_WIDTH; ++i)Pvalue += ds_M[ty][i] * ds_N[i][tx];
__synchthreads();
}
P[Row*Width+Col] = Pvalue;
}

## Slide 9: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, Int Width)
{
__shared__ float ds_M[TILE_WIDTH][TILE_WIDTH];
__shared__ float ds_N[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * blockDim.y + ty;
int Col = bx * blockDim.x + tx;
float Pvalue = 0;
// Loop over the M and N tiles required to compute the P element
for (int p = 0; p < n/TILE_WIDTH; ++p) {
// Collaborative loading of M and N tiles into shared memory
ds_M[ty][tx] = M[Row*Width + p*TILE_WIDTH+tx];
ds_N[ty][tx] = N[(t*TILE_WIDTH+ty)*Width + Col];
__syncthreads();
for (int i = 0; i < TILE_WIDTH; ++i)Pvalue += ds_M[ty][i] * ds_N[i][tx];
__synchthreads();
}
P[Row*Width+Col] = Pvalue;
}

## Slide 10: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, Int Width)
{
__shared__ float ds_M[TILE_WIDTH][TILE_WIDTH];
__shared__ float ds_N[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * blockDim.y + ty;
int Col = bx * blockDim.x + tx;
float Pvalue = 0;
// Loop over the M and N tiles required to compute the P element
for (int p = 0; p < n/TILE_WIDTH; ++p) {
// Collaborative loading of M and N tiles into shared memory
ds_M[ty][tx] = M[Row*Width + p*TILE_WIDTH+tx];
ds_N[ty][tx] = N[(t*TILE_WIDTH+ty)*Width + Col];
__syncthreads();
for (int i = 0; i < TILE_WIDTH; ++i)Pvalue += ds_M[ty][i] * ds_N[i][tx];
__synchthreads();
}
P[Row*Width+Col] = Pvalue;
}

## Slide 11: Tile (Thread Block) Size Considerations
Each thread block should have many threads
  TILE_WIDTH of 16 gives 16*16 = 256 threads
  TILE_WIDTH of 32 gives 32*32 = 1024 threads
For 16, in each phase, each block performs 2*256 = 512 float loads from global memory for 256 * (2*16) = 8,192 mul/add operations. (16 floating-point operations for each memory load)
For 32, in each phase, each block performs 2*1024 = 2048 float loads from global memory for 1024 * (2*32) = 65,536 mul/add operations. (32 floating-point operation for each memory load)

## Slide 12: Shared Memory and Threading
For an SM with 16KB shared memory
  Shared memory size is implementation dependent!
  For TILE_WIDTH = 16, each thread block uses 2*256*4B = 2KB of shared memory.
  For 16KB shared memory, one can potentially have up to 8 thread blocks executing
    This allows up to 8*512 = 4,096 pending loads. (2 per thread, 256 threads per block)
  The next TILE_WIDTH 32 would lead to 2*32*32*4 Byte= 8K Byte shared memory usage per thread block, allowing 2 thread blocks active at the same time
    However, in a GPU where the thread count is limited to 1536 threads per SM, the number of blocks per SM is reduced to one!
Each __syncthread() can reduce the number of active threads for a block
  More thread blocks can be advantageous

## Slide 13
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.