## Slide 1: Module 4.5 - Memory and Data Locality
Handling Arbitrary Matrix Sizes in Tiled Algorithms

## Slide 2: Objective
To learn to handle arbitrary matrix sizes in tiled matrix multiplication
  Boundary condition checking
  Regularizing tile contents
  Rectangular matrices

## Slide 3: Handling Matrix of Arbitrary Size
The tiled matrix multiplication kernel we presented so far can handle only square matrices whose dimensions (Width) are multiples of the tile width (TILE_WIDTH)
  However, real applications need to handle arbitrary sized matrices.
  One could pad (add elements to) the rows and columns into multiples of the tile size, but would have significant space and data transfer time overhead.
We will take a different approach.

## Slide 4: Phase 1 Loads for Block (0,0) for a 3x3 Example
P0,1
P0,0
P1,0
P0,2
P1,1
P2,0
P2,2
P2,1
P1,2
M0,1
M0,0
M1,0
M0,2
M1,1
M2,0
M2,2
M2,1
M1,2
N0,1
N0,0
N1,0
N0,2
N1,1
N2,0
N2,2
N2,1
N1,2
M0,2
M1,2
N2,1
N2,0
Shared Memory
Shared Memory
Threads (1,0) and (1,1) need special treatment in loading N tile
Threads (0,1) and (1,1) need special treatment in loading M tile

## Slide 5: Phase 1 Use for Block (0,0) (iteration 0)
P0,1
P0,0
P1,0
P0,2
P1,1
P2,0
P2,2
P2,1
P1,2
M0,1
M0,0
M1,0
M0,2
M1,1
M2,0
M2,2
M2,1
M1,2
N0,1
N0,0
N1,0
N0,2
N1,1
N2,0
N2,2
N2,1
N1,2
M0,2
M1,2
N2,1
N2,0
Shared Memory
Shared Memory

## Slide 6: Phase 1 Use for Block (0,0) (iteration 1)
P0,1
P0,0
P1,0
P0,2
P1,1
P2,0
P2,2
P2,1
P1,2
M0,1
M0,0
M1,0
M0,2
M1,1
M2,0
M2,2
M2,1
M1,2
N0,1
N0,0
N1,0
N0,2
N1,1
N2,0
N2,2
N2,1
N1,2
M0,2
M1,2
N2,1
N2,0
Shared Memory
Shared Memory
All Threads need special treatment. None of them should introduce invalidate contributions to their P elements.

## Slide 7: Phase 0 Loads for Block (1,1) for a 3x3 Example
P0,1
P0,0
P1,0
P0,2
P1,1
P2,0
P2,2
P2,1
P1,2
M0,1
M0,0
M1,0
M0,2
M1,1
M2,0
M2,2
M2,1
M1,2
N0,1
N0,0
N1,0
N0,2
N1,1
N2,0
N2,2
N2,1
N1,2
M2,1
M2,0
N0,2
N1,2
Shared Memory
Shared Memory
Threads (0,1) and (1,1) need special treatment in loading N tile
Threads (1,0) and (1,1) need special treatment in loading M tile

## Slide 8: Major Cases in Toy Example
Threads that do not calculate valid P elements but still need to participate in loading the input tiles
  Phase 0 of Block(1,1), Thread(1,0), assigned to calculate non-existent P[3,2] but need to participate in loading tile element N[1,2]
Threads that calculate valid P elements may attempt to load non-existing input elements when loading input tiles
  Phase 0 of Block(0,0), Thread(1,0), assigned to calculate valid P[1,0] but attempts to load non-existing N[3,0]

## Slide 9: A “Simple” Solution
When a thread is to load any input element, test if it is in the valid index range
  If valid, proceed to load
  Else, do not load, just write a 0
Rationale: a 0 value will ensure that that the multiply-add step does not affect the final value of the output element
The condition tested for loading input elements is different from the test for calculating output P element
  A thread that does not calculate valid P element can still participate in loading input tile elements

## Slide 10: Phase 1 Use for Block (0,0) (iteration 1)
P0,1
P0,0
P1,0
P0,2
P1,1
P2,0
P2,2
P2,1
P1,2
M0,1
M0,0
M1,0
M0,2
M1,1
M2,0
M2,2
M2,1
M1,2
N0,1
N0,0
N1,0
N0,2
N1,1
N2,0
N2,2
N2,1
N1,2
0
M0,2
M1,2
0
N2,1
N2,0
0
0
Shared Memory
Shared Memory

## Slide 11: Boundary Condition for Input M Tile
Each thread loads
  M[Row][p*TILE_WIDTH+tx]
  M[Row*Width + p*TILE_WIDTH+tx]
Need to test
  (Row < Width) && (p*TILE_WIDTH+tx < Width)
  If true, load M element
  Else , load 0
A
TILE_WIDTH
TILE_WIDTH

## Slide 12: Boundary Condition for Input N Tile
Each thread loads
  N[p*TILE_WIDTH+ty][Col]
  N[(p*TILE_WIDTH+ty)*Width+ Col]
Need to test
  (p*TILE_WIDTH+ty < Width) && (Col< Width)
  If true, load N element
  Else , load 0
B
TILE_WIDTH
TILE_WIDTH

## Slide 13: Loading Elements – with boundary check
8 for (int p = 0; p < (Width-1) / TILE_WIDTH + 1; ++p) {
++ if(Row < Width && t * TILE_WIDTH+tx < Width) {
9 ds_M[ty][tx] = M[Row * Width + p * TILE_WIDTH + tx];
++ } else {
++ ds_M[ty][tx] = 0.0;
++ }
++ if (p*TILE_WIDTH+ty < Width && Col < Width) {
10 ds_N[ty][tx] = N[(p*TILE_WIDTH + ty) * Width + Col];
++ } else {
++ ds_N[ty][tx] = 0.0;
++ }
11 __syncthreads();

## Slide 14: Inner Product – Before and After
++ if(Row < Width && Col < Width) {
12 for (int i = 0; i < TILE_WIDTH; ++i) {
13 Pvalue += ds_M[ty][i] * ds_N[i][tx];
}
14 __syncthreads();
15 } /* end of outer for loop */
++ if (Row < Width && Col < Width)
16 P[Row*Width + Col] = Pvalue;
} /* end of kernel */

## Slide 15: Some Important Points
For each thread the conditions are different for
  Loading M element
  Loading N element
  Calculating and storing output elements
The effect of control divergence should be small for large matrices

## Slide 16: Handling General Rectangular Matrices
In general, the matrix multiplication is defined in terms of rectangular matrices
  A j x k M matrix multiplied with a k x l N matrix results in a j x l P matrix
We have presented square matrix multiplication, a special case
The kernel function needs to be generalized to handle general rectangular matrices
  The Width argument is replaced by three arguments: j, k, l
  When Width is used to refer to the height of M or height of P, replace it with j
  When Width is used to refer to the width of M or height of N, replace it with k
  When Width is used to refer to the width of N or width of P, replace it with l

## Slide 17
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.