## Slide 1: Module 6.1 – Memory Access Performance
DRAM Bandwidth
Accelerated Computing
GPU Teaching Kit

## Slide 2: Objective
To learn that memory bandwidth is a first-order performance factor in a massively parallel processor
  DRAM bursts, banks, and channels
  All concepts are also applicable to modern multicore processors

## Slide 3: Global Memory (DRAM) Bandwidth
Ideal
Reality

## Slide 4: DRAM Core Array Organization
Each DRAM core array has about 16M bits
Each bit is stored in a tiny capacitor made of one transistor
Memory Cell
Core Array
Row
Decoder
Sense Amps
Column Latches
Mux
Row
Addr
Column
Addr
Off-chip Data
Wide
Narrow
Pin Interface

## Slide 5: A very small (8x2-bit) DRAM Core Array
decode
0
1
1
Sense amps
Mux

## Slide 6: DRAM Core Arrays are Slow
Reading from a cell in the core array is a very slow process
  DDR: Core speed = ½ interface speed
  DDR2/GDDR3: Core speed = ¼ interface speed
  DDR3/GDDR4: Core speed = ⅛ interface speed
  … likely to be worse in the future
decode
To sense amps
A very small capacitance that stores a data bit
About 1000 cells connected to each vertical line

## Slide 7: DRAM Bursting
For DDR{2,3} SDRAM cores clocked at 1/N speed of the interface:
  Load (N × interface width) of DRAM bits from the same row at once to an internal buffer, then transfer in N steps at interface speed
  DDR3/GDDR4: buffer width = 8X interface width

## Slide 8: DRAM Bursting Timing Example
time
Address bits to decoder
Core Array access delay
bits
on interface
Non-burst timing
Burst timing
Modern DRAM systems are designed to always be accessed in burst mode. Burst bytes are transferred to the processor but discarded when accesses are not to sequential locations.

## Slide 9: Multiple DRAM Banks
decode
Sense amps
Mux
decode
Sense amps
Mux
Bank 0
Bank 1

## Slide 10: DRAM Bursting with Banking
Single-Bank burst timing, dead time on interface
Multi-Bank burst timing, reduced dead time

## Slide 11: GPU off-chip memory subsystem
NVIDIA GTX280 GPU:
  Peak global memory bandwidth = 141.7GB/s
Global memory (GDDR3) interface @ 1.1GHz
  (Core speed @ 276Mhz)
  For a typical 64-bit interface, we can sustain only about 17.6 GB/s (Recall DDR - 2 transfers per clock)
  We need a lot more bandwidth (141.7 GB/s) – thus 8 memory channels

## Slide 12
GPU Teaching Kit
The GPU Teaching Kit is licensed by NVIDIA and the University of Illinois under the Creative Commons Attribution-NonCommercial 4.0 International License.